## Slide 1: General Method of Obstacle Detection and Avoidance Using GoPiGo
Undergraduate Research 4000
Junjie Liao
Dr.DeWitt
Notes: Decribe what a gopigo is

## Slide 2: Goal
Make GoPiGo move forward and avoid obstacles by turning around them.
  Using face detection to detect obstacles
  Avoidance with turning

## Slide 3: Face Detection
Viola-Jones algorithm
OpenCV
(Opencv.org)
Notes: Describe what’s doing: like filtering, one pattern is eyes are dark and the cheeks are light;
Light bridge and dark eyes for the second one

## Slide 4: Motions of GoPiGo
Moving straight
Turning with specified speed, radius, angle

## Slide 5: Moving Straight
Calibration of two motors
Convert a given linear speed into a motor parameter
  set_left_speed(parameter)
  set_right_speed(parameter)
  Parameter: 0 - 255
Notes: Parameter is just the function from gopigo library

## Slide 6: Calibration
Chart: Left Motor Parameter vs Speed
| 0.053925455294177 | 0.0757893947558627 | 0.097486859120404 | 0.121584734408594 | 0.145792473445035 | 0.169786213844637
 | 30 | 40 | 50 | 60 | 70 | 80
Chart: Right Motor Parameter vs Speed
| 0.0517203251520359 | 0.0737798274706694 | 0.0977804942382365 | 0.118047723953071 | 0.131075871145738 | 0.156650108189293
 | 30 | 40 | 50 | 60 | 70 | 80

## Slide 7: Turning Strategy
Needs to find out the distance between the GoPiGo and obstacles first
Two methods of turning were explored:
  Adjust the speed difference between two motors to make it turn with specified radius, speed and angle
  Using polygons to approximate a circle
Turning through a given angle

## Slide 8: Approximate The Distance To GoPiGo
Actual_width
Image_width
lens
Actual distance
d
Notes: D: is the distance between the lens and image censor, which has to be calibrated for further use

## Slide 9: First Turning Method
R
V_outer = (R+w/2)/(R-w/2)*V_inner
w
V_outer
V_inner
Notes: Talk about the issue which is the sliding, slipping

## Slide 10: Second Turning Method
R
Move forward for t_fwd
Turn left/right for t_turn
Notes: Points out gopigo has built-in function for it to stop and turns, and that’s cause the sharp corner

## Slide 11: Prioritizing Obstacle
Notes: Talks about a about 1-2 second delay, kinds of slow

## Slide 12: Problems
Even after calibration, GoPiGo still does not move in a straight line – seems to be affected by the surface of the paths
Avoidance strategy only based on the closest obstacle, but we want to find the best path that takes into account all obstacles
Face detection isn’t a 100% accurate, for example white board will be detected occasionally; besides, only frontal face will be detected
Takes a little more than one second to do the image analysis, which is slow
Notes: Might needs to talk about the board issue by drawing sth on it

## Slide 13: Future Work
A better response mechanism for motors in order to move forward in a more straight line
Make it able to go automatically with a given goal location using fictitious force model
Notes: Might need to draw it out on the board

## Slide 14: Acknowledgements
High Point University Physics Department
Dr.DeWitt

## Slide 15: Work Cited
opencv.org